## Slide 1: QM69A Inline Auto Diagnostic
F10 Data Scientists

## Slide 2: Agenda
Project Scope
QM69A overall Architecture
Data Engineering
  Teradata Data Transformation
  TDCH
  Hadoop Data Transformation
    Sigma Reader
    Non sigma Reader
    Combiner
Data Analytics
Data Visualization
Project Deployment Status
Future Enhancement

## Slide 3
This project aims to provide engineers with the most probable root cause(s) of a Out of Control (OOC) point in the SPACE (Inline) control chart.
Upon result validation, engineers can act in order to mitigate the cause of the OOC.
Project Scope

## Slide 4
QM69A overall Architecture

## Slide 5: Data Preparation

## Slide 6
Teradata to Hadoop: TDCH

## Slide 7
TeraData Connector for Hadoop
High-performance parallel bi-directional data movements
TDCH utilizes MapReduce as its execution engine
3 stages
Preprocessing - setup for source and target system
Post-processing - Clean up source and target system
Data Transfer - MapReduce
TDCH

## Slide 8
QM69A
TDCH
Read the last
loaded timestamp
Temp tables
BTEQ
Teradata query
Update the timestamp
Read the timestamp as start time
Get the latest datetime of specific dataset as end time
Query data from start time to end time in Teradata
Load data into Hbase via TDCH
Update the timestamp file
Iterate
Work Flow

## Slide 9
Table Name | Column Family | Row Key | Column Design | Table desc
eng_mti_${site}_fab_${fab_no}_GenericQueryData : sigma_lot_v3 | 1 | Lot ID | Run_complete_datetime+step_no+attribute Run_complete_datetime+step_no+test_dwid | 
TDCH
Sigma Data Ingest

## Slide 10
Table Name | Column Family | Row Key | Column Design | Table desc
eng_mti_${site}_fab_${fab_no}_GenericQueryData : sigma_wafer_v3 | 1 | Lot ID + Wafer ID | Run_complete_datetime+step_no+attribute Run_complete_datetime+step_no+test_dwid | Contains All the wafer level information as listed above
TDCH
Sigma Data Ingest(cont)

## Slide 11
Table Name | Column Family | Row Key | Column Design | Table desc
eng_mti_${site}_fab_${fab_no}_GenericQueryData : lot_v5 | 1 | Lot ID | AQT+From_step+To_step+AQT_item CT+Step_name+CT_item QT+From_step+To_step+AQT_item LA+corr_item_desc+sequence_no MB+Traveler_step+Chemical+sequence_no | Contains lot level information of AQT, CT, QT, LA & MB
Non-Sigma Data Ingest

## Slide 12
Table Name | Column Family | Row Key | Column Design | Table desc
eng_mti_${site}_fab_${fab_no}_GenericQueryData : wafer_v4 | 1 | Lot ID + Wafer ID | WA+corr_item_desc QDR+QDR_item+step_no SWR+SWR_item+step no | Contains All the wafer level information as listed above
Non-Sigma Data Ingest(cont)

## Slide 13
Table Name | Column Family | Row Key | Column Design | Table desc
eng_mti_${site}_fab_${fab_no}_GenericQueryData : qm69_report_v1 | 1 | QDR ID SWR ID | QDR SWR_STEPS | Contains All the report information as listed above
Non-Sigma Data Ingest(cont)

## Slide 14
Teradata to Hadoop: TDCH

## Slide 15
Reference table for
  Process Step (Daily Update)
  Material Batch Attributes (One Time Ingestion)
  SWR / QDR Attributes (One Time Ingestion)
  CT / QT Attributes (One Time Ingestion)
To optimize the cost of column qualifier storage
What is QM69A Dictionary (lookup)

## Slide 16
HIVE SPACE OOC

## Slide 17
HIVE SPACE OOC
space_bad_charts_new |  | 
Headers | Data Type | Example Values
fab | string | 10
module | string | CVD, PVD, IMPLANT, PHOTO, WET PROCESS, DIFFUSION, CMP, DRY ETCH, METRO
design_id | string | B16A
ch_id | int | 436476
current_step | string | 1210-23 PERIPH PHOTO SEM CD
process_step | string | 3010-23 PERIPH PHOTO
parameter_name | string | CD1_SPACE_BOT
lot_id | string | 8064111.001
wafer_id | string | 4111-25 (for lot level chart this column is '-' or '.')
label | int | space_ooc_label: 0,1
value | double | measurement_value
sample_date | timestamp | some_date
ucl | double | upper_control_limit
lcl | double | lower_control_limit
col_type | string | Production,Qual
channel_type | string | Area,PML,Engineering
chart_type | string | Mean,Sigma,Range,EWMA
clusterid | string | 1,2,3…
clusterlabel | string | B/G
last_ooc_date | timestamp | some_date
ooc_property | string | NA,H,L
session_id | string | 20160703-2200

## Slide 18
Non-Sigma Reader

## Slide 19
Column Names | Description | Example
Module | Eg. CMP, CVD | PHOTO
Ch_id | SPACE chart channel ID | 82331
Current_step | Measurement Step | 1200-53 PERIPH PHOTO RINSE REG
Process_Step | Process Step | 3010-53 PERIPH PHOTO
Lot_id |  | 7454007.027
Wafer_id |  | 4007-08
Label | OOC cluster label (1 for BAD 0 for GOOD) | 0
Value | SPACE chart measurement value | 1.27292375182328
Sample_date | Sampling date | 2016-10-15 23:37:26
UCL | (Upper control Limit) | 3.4
LCL | (Lower Control Limit) | 0.521503453
Chart_type | Chart Type, i.e.Mean , EWMA | Sigma
Cluster_id | OOC cluster ID | 36
Cluster_label | B – Bad ; G – Good | G
Last_ooc_date | Last OOC date of the SPACE chart | 2016-10-17 00:12:11
Signal (Features) | Features from the HBASE (QT, CT, Process, Tool) | QDR:XXXXXXX
Signal value (Feature value) | Feature value from the HBASE | 1
Non-Sigma Reader

## Slide 20
Sigma Reader

## Slide 21
Sigma Reader
Column Names | Description | Example
Module | Eg. CMP, CVD | PHOTO
Ch_id | SPACE chart channel ID | 82331
Current_step | Measurement Step | 1200-53 PERIPH PHOTO RINSE REG
Process_Step | Process Step | 3010-53 PERIPH PHOTO
Lot_id |  | 7454007.027
Wafer_id |  | 4007-08
Label | OOC cluster label (1 for BAD 0 for GOOD) | 0
Value | SPACE chart measurement value | 1.27292375182328
Sample_date | Sampling date | 2016-10-15 23:37:26
UCL | (Upper control Limit) | 3.4
LCL | (Lower Control Limit) | 0.521503453
Chart_type | Chart Type, i.e.Mean , EWMA | Sigma
Cluster_id | OOC cluster ID | 36
Cluster_label | B – Bad ; G – Good | G
Last_ooc_date | Last OOC date of the SPACE chart | 2016-10-17 00:12:11
Signal (Features) | Features from the HBASE (QT, CT, Process, Tool) | process::4800-00 PWELL OXIDATION::GeRM PROCESS - RUN_ATTR::1
Signal value (Feature value) | Feature value from the HBASE | OX_THERMAL_95A_900C_600T_DRY_no_Cl_REVD
Violation Direction | Refers to the location of the OOC point | 1
Step Seq | This is the step sequence of the entire traveler flow. | 3600

## Slide 22
Combiner Reader

## Slide 23
Combiner Reader
Column Names | Description | Example
Module | Eg. CMP, CVD | PHOTO
Ch_id | SPACE chart channel ID | 82331
Current_step | Measurement Step | 1200-53 PERIPH PHOTO RINSE REG
Process_Step | Process Step | 3010-53 PERIPH PHOTO
Lot_id |  | 7454007.027
Wafer_id |  | 4007-08
Label | OOC cluster label (1 for BAD 0 for GOOD) | 0
Value | SPACE chart measurement value | 1.27292375182328
Sample_date | Sampling date | 2016-10-15 23:37:26
UCL | (Upper control Limit) | 3.4
LCL | (Lower Control Limit) | 0.521503453
Chart_type | Chart Type, i.e.Mean , EWMA | Sigma
Cluster_id | OOC cluster ID | 36
Cluster_label | B – Bad ; G – Good | G
Last_ooc_date | Last OOC date of the SPACE chart | 2016-10-17 00:12:11
Signal (Features) | Features from the HBASE (QT, CT, Process, Tool) | process::4800-00 PWELL OXIDATION::GeRM PROCESS - RUN_ATTR::1
Signal value (Feature value) | Feature value from the HBASE | OX_THERMAL_95A_900C_600T_DRY_no_Cl_REVD
Violation Direction | Refers to the location of the OOC point | 1
Step Seq | This is the step sequence of the entire traveler flow. | 3600

## Slide 24: Analytic and Report

## Slide 25
Data Analysis

## Slide 26
Overall Flow
Data Analysis

## Slide 27
  Pre-process
  Pivot chart information locally
  Reclassify OOC points with loose criteria
  Filter charts without enough OOC points
  Filter Features with zero variance
Data Analysis(cont)

## Slide 28
  Why Random Forest
  Feature importance can be easily interpreted compared with other supervised learning model (neural network, SVM…)
  With comparable prediction power, the training is faster compare with other method.
  Parameters tuning is more robust.
  Always return result based on the relative importance no matter how weak the correlation is
Data Analysis(cont)

## Slide 29
  Why Classifier
  We are more interested in OOC and almost OOC points than the correlation between target SPACE measurement and signals.
  Regression correlation detected may not be the cause of the OOC instance
Data Analysis(cont)

## Slide 30
  Why Kruskal Wallis Test (a.k.a H test)
  Random Forest Classifier always returns results, since the feature important list is a ranking of relative importance.
  Kruskal Wallis Test is a non-parametric hypothesis test
    Does not assume your data comes from a particular distribution
    No minimum sample size is required
    Compare the ranking of value in each group, hence minimize the impact of outliers
Data Analysis(cont)

## Slide 31
  Post-process
  Further filter result by checking the percentile of the flagged features
    Higher group’s 25 percentile must be greater than lower group’s 75 percentile
SPC measurement
SPC measurement
IS IS NOT
IS IS NOT
Data Analysis(cont)

## Slide 32
Reporting Report Generator

## Slide 33
Reporting Report Generator
Output Schema from Random Forest Analytics
Ch_Id
Chart Type
Module
Importance_Score
Signal (Feature of Importance)
Status
Violation Direction
  Analytic Result only contains the important features of the successfully diagnosed charts
  More raw data are required for visualization.
  Report should contain result for all charts

## Slide 34
Final Tableau Report

## Slide 35
Final Tableau Report

## Slide 36
Site | Data Ingestion | Analytic | Reporting
Fab 10W | Up & Running | Up & Running | Up & Running
Fab 10N | Up & Running | Up & Running | Up & Running
Fab 15 | Up & Running | Not Started | Not Started
Fab 16 | Up & Running | Not Started | Not Started
Deployment Status

## Slide 37
  Package is ready for deployment at stash:
  https://stash.micron.com/bbdc/projects/QM69/repos/qm69a/browse
Package Availability

## Slide 38
  Replace the heavily Hbase put method to bulk loading when feeding data into Hbase to release the load of zookeeper
  Move the quantile check to pre-processing to minimize the data for local pivot, so that improve the memory efficiency and speed.
  Replace random forest by other well distributed algorithm with comparable accuracy. (in experiment phase)
  Tier 2 Implemetation
Future optimization

## Slide 41: Appendix

## Slide 42: Issues and Error Encountered

## Slide 43: Cluster Dependent Problem
Hbase Connection Reset Issue
  Cause: Still open for IT to further investigate
  Action: Raise remedy if encountered
Server returns error 12
  Cause: Too many process running on the edge node
  Action: Remedy to the UNIX team
HBASE region server slowness Mapper jobs are not given containers to start.
  Cause: Normally caused be overloaded Cluster.
  Action: Submit remedy to report the problem and re-run the session when cluster is back to normal

## Slide 44: Analytic related Problem
Status of record starts with “Error: ”
  Cause: Unexpected data detected in the analytic script/ defect in the script
  Action: Validate the input data to analytic script
Failed to connect to certain executor/Failed to write/Missing output location for shuffle
  Cause: Cluster condition dependent
  Action: Submit remedy to report the problem and re-run the session when cluster is back to normal

## Slide 45: Table Schema

## Slide 46: Datasets (AQT)
Column Design : AQT+From_step+To_step+AQT_item
FAB_${FAB}_FT_DM.FAB_LOT_HIST
FAB_${FAB}_TRV_DM.TRAV_STEP
FAB_${FAB}_QTL_DM.QTL_STEP_GROUP
FAB_${FAB}_REF_DM.STEP
Lot_id
Trav_step_oid
Tracked_in_datetime
Tracked_out_datetime
Trav_step_oid
Step_oid
Step_oid
Step_name
step_group_name

## Slide 47: Datasets (QT)
FAB_${FAB}_QTL_DM.LOT_BREACH

## Slide 48: Datasets (CT)
FAB_${FAB}_FT_DM.FAB_LOT_HIST
FAB_${FAB}_REF_DM.STEP
FAB_${FAB}_TRV_DM.TRAV_STEP
Lot_id
Stage_datetime
Track_in_datetime
Track_out_datetime
Trav_step_oid
Updated_datetime
Step_name
Step_oid
Trav_step_oid
Step_oid
RPT = track_out_datetime – track_in_datetime
Cycle_Time = track_out_datetime – stage_datetime
Waiting_Time = track_in_datetime – stage_datetime
Stage_datetime = Previous Step Track out Time

## Slide 49: Datasets (LA)
FAB_${FAB}_FT_DM.FAB_LOT_ATTR_LOG
FAB_${FAB}_REF_DM.CORR_ITEM
Lot_id
…
Corr_item_oid
Seq_no
Corr_item_value
Corr_item_desc
Corr_item_oid
Column Design: LA+corr_item_desc+sequence_no

## Slide 50: Dataset (WA)
FAB_16_FT_DM.WAFER_STATUS
FAB_16_FT_DM.WAFER_ATTR
FAB_16_REF_DM.CORR_ITEM
Lot_id
Wafer_id
Wafer_scribe
Wafer_scribe
Wafer_attr_value
Updated_datetime
Corr_item_oid
Corr_item_desc
Corr_item_oid
Column Design: WA+corr_item_desc

## Slide 51: Datasets (SWR)
Column Design: SWR+SWR_item+step no

## Slide 52: Datasets (QDR)
Column Design: QDR+QDR_item+step_no

## Slide 53: Datasets (SWR_report)
Column Design: SWR_STEPS

## Slide 54: Datasets (QDR_report)
Column Design: QDR

## Slide 55: Datasets (MB)
Column Design: MB+Traveler_step+Chemical+sequence_no

## Slide 56: Datasets (Sigma)
1
2
1.
2.
lot_ID | Run_complete_datetime | Step_no | Attribute | timestamp | value
lot_ID | Run_complete_datetime | Step_no | Test_dwid | timestamp | value
Lookup in HBase lookup table
Lookup in sigma_test_def table
Lookup in HBase lookup table

## Slide 57: eng_mti_singapore_fab_10_autodiagnostic.space_ooc_summary_qm69a_new
Input
Output
Table Name | Extracted Info
idl_t_channel_def | basic channel background info
idl_samples_viol | violation details
space_ooc_summary_qm69a_new | 
Column Name | Format
fab | string
module | string
ch_id | int
col_type | string
channel_type | string
chart_type | string
ooc | int
session_id | string

## Slide 58: eng_mti_singapore_fab_10_autodiagnostic.space_clustering_data_qm69a_new
Table Name | Extracted Info
idl_t_channel_def | basic channel background info
idl_samples_calc | ewma data, ucl, lcl
idl_samples_viol | violation details
idl_samples_wafer | wafer level mean chart data
idl_samples_lot | wafer level mean chart data
space_clustering_data_qm69a_new | 
Column Name | Format
fab | string
module | string
design_id | string
ch_id | int
current_step | string
process_step | string
parameter_name | string
lot_id | string
wafer_id | string
label | string
value | string
sample_date | string
ucl | string
lcl | string
col_type | string
channel_type | string
chart_type | string
session_id | string
Table Name | Extracted Info
space_ooc_summary_qm69a_new | Which channel and chart to query
Input
Output

## Slide 59: eng_mti_singapore_fab_10_autodiagnostic.space_clustering_result_qm69a_new
Table Name
space_clustering_data_qm69a_new
space_bad_charts_new | 
Headers | Data Type
fab | string
module | string
design_id | string
ch_id | string
current_step | string
process_step | string
parameter_name | string
lot_id | string
wafer_id | string
label | string
value | string
sample_date | string
ucl | string
lcl | string
col_type | string
channel_type | string
chart_type | string
clusterid | string
clusterlabel | string
last_ooc_date | string
ooc_property | string
session_id | string
Application Name
OOC clustering (Jane)
Input
Output

## Slide 60: eng_mti_singapore_fab_10_autodiagnostic.space_clustering_result_qm69a_new_trunc
Table Name
space_clustering_result_qm69a_new
space_bad_charts_new | 
Headers | Data Type
fab | string
module | string
design_id | string
ch_id | string
current_step | string
process_step | string
parameter_name | string
lot_id | string
wafer_id | string
label | string
value | string
sample_date | string
ucl | string
lcl | string
col_type | string
channel_type | string
chart_type | string
clusterid | string
clusterlabel | string
last_ooc_date | string
ooc_property | string
session_id | string
Application Name
OOC Truncation pyspark
Input
Output

## Slide 61: eng_mti_singapore_fab_10_autodiagnostic.space_bad_charts_new
Table Name
space_clustering_result_qm69a_new
space_bad_charts_new |  | 
Headers | Data Type | Example Values
fab | string | 10
module | string | CVD, PVD, IMPLANT, PHOTO, WET PROCESS, DIFFUSION, CMP, DRY ETCH, METRO
design_id | string | B16A
ch_id | int | 436476
current_step | string | 1210-23 PERIPH PHOTO SEM CD
process_step | string | 3010-23 PERIPH PHOTO
parameter_name | string | CD1_SPACE_BOT
lot_id | string | 8064111.001
wafer_id | string | 4111-25 (for lot level chart this column is '-' or '.')
label | int | space_ooc_label: 0,1
value | double | measurement_value
sample_date | timestamp | some_date
ucl | double | upper_control_limit
lcl | double | lower_control_limit
col_type | string | Production,Qual
channel_type | string | Area,PML,Engineering
chart_type | string | Mean,Sigma,Range,EWMA
clusterid | string | 1,2,3…
clusterlabel | string | B/G
last_ooc_date | timestamp | some_date
ooc_property | string | NA,H,L
session_id | string | 20160703-2200
Input
Final Output