## Slide 1: Inline AD Introduction
Tan Peng
2019/05/22

## Slide 2: Current AD Team
Tan Peng
Zhou Siqi
Khoo Kaiqin
Beverly

## Slide 3: Agenda
Background
Manual OOC root cause analysis
Inline AD analysis and ORION AD analysis
Challenges and Future Plan

## Slide 4: Inline Auto Diagnostics
Background
SPC
SPACE Charts

## Slide 5: Inline Auto Diagnostics
Background
Out-of-Control
(OOC) Points
Out-of-Control
(OOC) Limit

## Slide 6: Inline Auto Diagnostics
Background
What is the root cause of these OOCs?

## Slide 7: Manual Diagnostics
How engineers normally do the diagnostics?
SPACE Match
FMEA
Domain
Tool Commonality
Incoming measurement drift
Important tool parameters
Qual History
PM/CM Records
R2R Tuning History
SWR/Conversion

## Slide 8: Overall Inline AD Flow
Search Charts to Analysis
Collect SPACE data/Sigma data and other data
Perform AD Analysis
Generate AD Report
Daily Scan,~6 hour data latency, each report generation takes ~5 min

## Slide 9: Overall ORION AD Flow
eCAP Trigger
Collect data from stream cluster
Perform AD Analysis
Generate AD Report
Triggering based, ~15 min data latency, each report generation takes < 3 min

## Slide 10
Search Charts to Analysis
Collect data
AD Analysis
Generate Report
SPC Hive Table
Channel 123456, CKC 0
Channel 123458, CKC 1
…
Find Channel/CKC has OOC in
Past 24 hours

## Slide 11
HBase
  Sigma
    Tool
    Recipe
    …
Teradata
  SWR
  QDR
  Lot Attribute
  PM/CM Records
  Wafer Genealogy
Reference File
  FMEA step list
Domain
  Domain step
Past Feedback
Search Charts to Analysis
Collect data
AD Analysis
Generate Report

## Slide 12
After collecting all data, we need to manipulate the data into an analysis-friendly format
Search Charts to Analysis
Collect data
AD Analysis
Generate Report
Lot_id | Wafer_id | Label | Step1 tool1 | Step1 tool2 | Step1 recipe1
1234567.001 | 4567-01 | 0 | 1 | 1 | 1
1234567.001 | 4567-02 | 1 | 0 | 0 | 0
1234568.001 | 4568-02 | 0 | 1 | 0 | 1
1234569.001 | 4569-01 | 1 | 1 | 1 | 0

## Slide 13
We try to find the “best” item correlated to OOC
Search Charts to Analysis
AD Analysis
Generate Report
Collect data
Lot_id | Wafer_id | Label | Step1tool1 | Step1tool2 | step1recipe1
1234567.001 | 4567-01 | 0 | 1 | 1 | 1
1234567.001 | 4567-02 | 1 | 0 | 0 | 0
1234568.001 | 4568-02 | 0 | 1 | 0 | 1
1234569.001 | 4569-01 | 1 | 1 | 1 | 0

## Slide 14
Time Weighted Correlation (Link)
Search Charts to Analysis
AD Analysis
Generate Report
Collect data
Equal weighted
Time weighted

## Slide 15
Categorize step
Top 3 correlation from each category are selected
Search Charts to Analysis
AD Analysis
Generate Report
Collect data
FMEA
Past Lesson Step
Process Step
Measurement Step
At Loop
Incoming
Domain Step

## Slide 16
Search Charts to Analysis
Collect data
AD Analysis
Generate Report

## Slide 17
Search Charts to Analysis
Collect data
AD Analysis
Generate Report
Feedback system is embedded into this report
Result will send back to MSSQL to track.

## Slide 18: Challenges
Too many potential root causes
Prefer ad-hoc analysis
Reduce data latency and analysis time further

## Slide 19: Future Plan
Limit potential root causes number < 3
Focus on ORION AD
R2R Tuning History
Use eCAP closure information as knowledge base

## Slide 20: Appendix
Confluence Page
  http://f10adintro/
Code Repo
  https://bitbucket.micron.com/bbdc/projects/FDS/repos/chronic_ad_v2/browse
  We build a few python packages/API to quick query space/sigma/lot attribute etc..
Dashboard
  https://tableau-apac/#/site/F10FEMFG/views/F10_QM69A_V2_RDA_OOC_SUMMARY/AD?:iid=1
  https://tableau-apac/#/site/F10FEMFG/views/F10_CHRONIC_OOC_AD_SUMMARY/ChronicAD?:iid=1