## Slide 1: ORION AD Update
2/1/2019
Peng Tan / Siqi Zhou

## Slide 2: Agenda
Feature gap between existing ORION AD(production version) and ORION AD Beta (deployed for RDA AD and Chronic OOC AD)
  Triggering rule
  Data source
  Features
Future roadmap

## Slide 3: Comparison Summary
 |  | ORION AD | ORION AD Beta | 
 |  |  | RDA AD | PEE AD
Triggering rule |  | Real-time | scheduled daily | 
Data source | SPACE | in messages (max 30 points) | Hive (latency: ~3h) | 
 | Sigma | streaming cluster, HBase, sigma (data latency: <15 mins) | prod cluster, HBase, sigma (data latency: 40mins~1h) | 
 | Teradata | N/A | new datasets SWR/QDR/lot attribute/PM_CM checking are using Teradata | 
Feature | Basic checking | pair correlation | pair correlation | 
 | Accuracy improvement | N/A | time weighted analysis | 
 |  |  | FMEA | N/A
 |  |  | domain knowledge | domain knowledge
 |  |  | past lesson learnt / users’ feedback | 
 | Further accuracy improvement (adding in new datasets) | N/A | new datasets SWR/QDR/lot attribute | 
 |  |  | PM/CM checking | 
 |  |  | Test wafer build traveler analysis | 
 | friendly UI | N/A | plot enhancement | 
 | Reduce false alarms / Provide more meaningful root causes / Smarter AD | N/A | channel level analysis | 
 |  |  | single context removal | 
 |  |  | curve trending detection | 

## Slide 4: Comparison 1 - Triggering Rule
 | ORION AD | ORION AD Beta | 
 |  | RDA AD | PEE AD
Triggering rule | Real-time | scheduled daily | scheduled daily
 | 1. Chart has minimum 2 OOC points and 2 good points in same chart type for 30 points. | 1. Chart has minimum 2 OOC points and 2 good points in same chart type for last 30 days. | 1. Chart has minimum 2 OOC points and 2 good points in same chart type for last 30 days.
 | 2. Chart types are mean, sigma, range and ewma-mean. | 2. Chart types are mean, sigma, range and ewma-mean. | 2. Chart types are mean, sigma, range and ewma-mean.
 | 3. Analyzed base on the chart type sequence: mean>sigma>range>ewma-mean. | 3. For multiple chart type highlighted in the Chronic OOC chart list, the chart type with most OOC points will be analyzed by AD. [1] | 3. For multiple chart type highlighted in the Chronic OOC chart list, the chart type with most OOC points will be analyzed by AD. [1]
 | 4. Trigger by per eCAP and also need to satisfy rule 1 above. | 4. Check whether there are at least 2 OOC points within 3 days. | 4. use Chronic OOC chart list from SPC team.
Reference:
[1] e.g. one chart was highlighted both in chart type ‘mean’ and ‘sigma’ and the assumption is the chart got more OOC points in ‘mean’ than ‘sigma’, AD will only trigger analysis for chart type ‘mean’.

## Slide 5: Comparison 2 - Data source
 |  | ORION AD | ORION AD Beta | 
 |  |  | RDA AD | PEE AD
Data source | SPACE | in messages (max 30 points) | Hive (latency: ~3h) | 
 | Sigma | streaming cluster, HBase, sigma (data latency: <15 mins) | prod cluster, HBase, sigma (data latency: 40mins~1h) | 
 | Teradata | N/A | new datasets SWR/QDR/lot attribute/PM_CM/Test wafer build traveler checking are using Teradata | 

## Slide 6: Comparison 3 - Feature
 |  | ORION AD | ORION AD Beta | 
 |  |  | RDA AD | PEE AD
Feature | Basic checking | pair correlation | pair correlation | 
 | Accuracy improvement | N/A | time weighted analysis | 
 |  |  | FMEA | N/A
 |  |  | domain knowledge | domain knowledge
 |  |  | past lesson learnt / users’ feedback | 
 | Further accuracy improvement (adding in new datasets) | N/A | new datasets SWR/QDR/lot attribute | 
 |  |  | PM/CM checking | 
 |  |  | Test wafer build traveler analysis | 
 | friendly UI | N/A | plot enhancement | 
 | Reduce false alarms / Provide more meaningful root causes / Smarter AD | N/A | channel level analysis | 
 |  |  | single context removal | 
 |  |  | curve trending detection | 

## Slide 7: Features

## Slide 8: Pair correlation
To better understand how correlation is calculated in above table, we use a simple example to illustrate:
  When we calculate the correlation between chamber 1 vs OOC, the value is -0.3. Low correlation.
  When we calculate the correlation between chamber 2 vs OOC, the value is 1. High correlation.
OOC | Chamber 1 | Chamber 2
1 | 0 | 1
1 | 1 | 1
1 | 0 | 1
0 | 1 | 0
0 | 0 | 0
0 | 1 | 0
Basic checking; Available in ORION/RDA/Chronic OOC AD

## Slide 9: Time weighted analysis
Accuracy improvement; Available in RDA/Chronic OOC AD
Weighted correlation (Link)
Equal weighted
Time weighted

## Slide 10: Time weighted analysis
Accuracy improvement; Available in RDA/Chronic OOC AD
RDA user Si Min gave a feedback that AD didn’t flag out equipment KOKUAGAO00.
This feature currently is available for both RDA AD and Chronic OOC AD.
  AD will focus on the latest OOCs.
  Toggles matches in the latest OOC time period will have much higher correlation value than early period.
  Current Rsquare value is calculated by this time weighted correlation. The higher Rsquare is, the better match between potential toggles and OOC points.

## Slide 11: Time weighted analysis
Before
After
Accuracy improvement; Available in RDA/Chronic OOC AD

## Slide 12: FMEA
Accuracy improvement; Available in RDA AD
This feature currently is only available for RDA AD.
  A list contains measurement step, process step and corresponding channel id.
  This list is prepared by RDA team so far.
  AD will check whether channel id is in the list and mark corresponding process step as FMEA step.
FMEA List Example
Measurement Step | Process Step | Channel Id
1000-82 PASS PHOTO MACRO INSP | 3010-82 PASS PHOTO | 716608
1000-82 PASS PHOTO MACRO INSP | 3010-82 PASS PHOTO | 716609
1000-82 PASS PHOTO MACRO INSP | 3010-82 PASS PHOTO | 716610
1000-82 PASS POLYIMIDE ANNEAL 2 WIS INSP | 3010-82 PASS PHOTO | 716616
1000-82 PASS POLYIMIDE ANNEAL 2 WIS INSP | 3010-82 PASS PHOTO | 716617
1000-82 PASS POLYIMIDE ANNEAL 2 WIS INSP | 3010-82 PASS PHOTO | 716618
1000-02 ALIGN MARK INSITU DRY STRIP MICRO INSP | 5200-23 PERIPH OXIDE CMP | 716622
1000-02 ALIGN MARK INSITU DRY STRIP MICRO INSP | 5200-23 PERIPH OXIDE CMP | 716623
1000-02 ALIGN MARK INSITU DRY STRIP MICRO INSP | 5200-23 PERIPH OXIDE CMP | 716624
1000-28 W0 METAL SPUTTER MICRO INSP | 3010-28 W0 PHOTO | 716628
1000-28 W0 METAL SPUTTER MICRO INSP | 3010-28 W0 PHOTO | 716631
1000-28 W0 METAL SPUTTER MICRO INSP | 3010-28 W0 PHOTO | 716632

## Slide 13: Domain knowledge
Accuracy improvement; Available in RDA AD /Chronic OOC AD
This feature currently is both RDA AD and Chronic OOC AD.
  A list contains RDA defect parameter and corresponding process step pattern.
  This list is prepared by RDA team so far.
  AD will check whether defect parameter is in the list and mark corresponding process step as Domain Knowledge step.
Domain Knowledge Example:
  “CB_32_RESIDUAL_FILM”: current loop CMP, WP or WET ETCH steps.
  “CB 19_RESIDUE”: current loop after PHOTO steps.

## Slide 14: Past lesson learnt / users’ feedback
Accuracy improvement; Available in RDA /Chronic OOC AD
This feature currently is available for both RDA AD and PEE AD.
AD will query past feedback cases for same chart and mark past feedback root cause step as feedback step

## Slide 15: New dataset SWR
Further accuracy improvement; Available in RDA /Chronic OOC AD
This feature is able to highlight SWR as the OOC root cause.
Data Source: Teradata
Good use case:

## Slide 16: New dataset QDR
Further accuracy improvement; Available in RDA /Chronic OOC AD
This feature is able to highlight QDR as the OOC root cause.
Data Source: Teradata
Good use case:

## Slide 17: New dataset lot attribute
Further accuracy improvement; Available in RDA/ Chronic OOC AD
This Lot Attribute feature is able to highlight lot attribute as the OOC root cause. Usually the lot attributes starting with Z (e.g. ZWPY36POSTSOFTSPRAY) are considered as conversion leading to excursion that users are afraid of.
Data Source: Teradata
Good use case:

## Slide 18: New dataset Test Wafer Build Traveler
Further accuracy improvement; Available in RDA/ Chronic OOC AD
This test wafer build traveler feature is able to highlight tool/recipe/… in test wafer build traveler as the OOC root cause.
Data Source: Teradata
Good use case:

## Slide 19: PM/CM checking
Further accuracy improvement; Available in RDA/Chronic OOC AD
This feature is aimed to correlate OOC points and PM/CM lead lot to boost up the confidence on root cause finding.
Checking criteria is that we use latest OOC lot and check whether this lot is the first two lots after certain PM/CM for certain step.
Good use case:

## Slide 20: Plot enhancement 1 for SWR/QDR/LT
Before
After
Friendly UI; Available in RDA /Chronic OOC AD
  Red label points (root cause) are not so obvious in terms of feature-lot attribute.
  Investigated the reasons are 1. Many points from different labels but with the same X-axis and Y-axis values are covered together leading to color mixture. 2. Raw data parsed into the result table for calculating the possibility of root cause got lots of duplicate.
  The final solutions are 1. adjusting the transparency of points and 2. dropping duplicate values of data frame. Optimization results are as the following figures in the next slice.

## Slide 21: Plot enhancement for SWR/QDR/LT
Friendly UI; Available in RDA /Chronic OOC AD
RDA user Si Min gave a feedback that LT analysis should provide only one label's data which is like the following good case, once this highlighted lot attribute came in, the total baseline changed meaning that it is true toggle. However, AD provides a mixture from many LTs which is not a normal way for user to judge root cause.

## Slide 22: Plot enhancement for SWR/QDR/LT
Before
After
Friendly UI; Available in RDA /Chronic OOC AD

## Slide 23: Channel level analysis
Reduce false alarms/Smarter AD; Available in RDA /Chronic OOC AD
This feature enables the channel level analysis in AD aimed to give a comparison between highlighted CKCs, which will help to identify incoming toggle and speed up troubleshooting for multiple CKC OOCs with similar issue.
  If ckc is not equal to 0, AD will query all samples based on the corresponding channel level.
PEE user Shaun gave the feedback that multiple CKCs highlighted got the same issue.
CKC level
Channel level / multiple CKCs

## Slide 24: Channel level analysis
Before
After
Reduce false alarms/Smarter AD; Available in RDA /Chronic OOC AD
Previous Report vs. After Report

## Slide 25: Plot enhancement for channel level analysis
Before
After
Friendly UI; Available in RDA /Chronic OOC AD
Potential Root Cause highlighted in bold red.
Some font size and legend optimization.

## Slide 26: Single context removal
Reduce false alarms/Smarter AD; Available in RDA /Chronic OOC AD
if root cause only has one recipe/process id/ etc. do not list in the root cause list. except they are from process step.

## Slide 27: Curve trending detection
Reduce false alarms/Smarter AD; Available in RDA /Chronic OOC AD
PEE gave us a feedback that most highlighted toggles are obviously wrong when looking at time trend in one AD report.

## Slide 28: Curve trending detection
Reduce false alarms/Smarter AD; Available in RDA/ /Chronic OOC AD
Why Step type filter?
  In order to make sure this new feature won’t filter out the correct found cases leading to decreasing accuracy.
  Currently many correct cases from users’ feedback are from FMEA/process step.
Why Single context filter?
  This feature needs to keep the same judgement as a new feature that we released recently for filtering the single context value in AD report.
  A special handling to make the code more robust: Single context filter is used for the case that non root cause datasets have less than 2 points meaning no slope.

## Slide 29: Curve trending detection
Before
After
AD repot link
AD repot link
Reduce false alarms/Smarter AD; Available in RDA /Chronic OOC AD
Comparison 1- Result table

## Slide 30: Curve trending detection
Before
After
Reduce false alarms/Smarter AD; Available in RDA/PEE AD
Comparison 1- plotting

## Slide 31: Curve trending detection
Before
After
Reduce false alarms/Smarter AD; Available in RDA /Chronic OOC AD
Comparison 2- Result table
AD repot link
AD repot link

## Slide 32: Curve trending detection
Before
After
Reduce false alarms/Smarter AD; Available in RDA /Chronic OOC AD
Comparison 2- plotting from 5_measurement_step
No highlight from 5_measurement_step

## Slide 33: Curve trending detection
Before
After
Reduce false alarms/Smarter AD; Available in RDA /Chronic OOC AD
Comparison 2- plotting from 7_incoming

## Slide 34: Comparison summary
 |  | ORION AD | ORION AD Beta | 
 |  |  | RDA AD | PEE AD
Triggering rule |  | Real-time | scheduled daily | 
Data source | SPACE | in messages (max 30 points) | Hive (latency: ~3h) | 
 | Sigma | streaming cluster, HBase, sigma (data latency: <15 mins) | prod cluster, HBase, sigma (data latency: 40mins~1h) | 
 | Teradata | N/A | new datasets SWR/QDR/lot attribute/PM_CM checking are using Teradata | 
Feature | Basic checking | pair correlation | pair correlation | 
 | Accuracy improvement | N/A | time weighted analysis | 
 |  |  | FMEA | N/A
 |  |  | domain knowledge | domain knowledge
 |  |  | past lesson learnt / users’ feedback | 
 | Further accuracy improvement (adding in new datasets) | N/A | new datasets SWR/QDR/lot attribute | 
 |  |  | PM/CM checking (future: Fault detection) | 
 | friendly UI | N/A | plot enhancement | 
 | Reduce false alarms / Provide more meaningful root causes / Smarter AD | N/A | channel level analysis | 
 |  |  | single context removal | 
 |  |  | curve trending detection | 

## Slide 35: Future Paln

## Slide 36: Plan and Roadmap
 |  | ORION AD | ORION AD (to be) | Timeline
Triggering rule |  | Real-time | Real-time | 
Data source | SPACE | in messages (max 30 points) | streaming cluster HBase | In Progress (temp solution will have data latency ~ 20min)
 | Sigma | streaming cluster, HBase, sigma (data latency: <15 mins) | streaming cluster, HBase, sigma (data latency: <15 mins) | Complete
 | SWR/QDR/Lot Attribute/Test Wafer Build Traveler | N/A | streaming cluster | In progress, target end of March
Feature | Basic checking | pair correlation | pair correlation | Complete
 | Accuracy improvement | N/A | time weighted analysis FMEA domain knowledge | Complete
 | Further accuracy improvement (adding in new datasets) | N/A | new datasets SWR/QDR/lot attribute PM/CM checking Test wafer build traveler analysis | Complete (Logic complete, pending IT to enable datasets in stream cluster)
 | friendly UI | N/A | plot enhancement | Complete
 | Reduce false alarms / Provide more meaningful root causes / Smarter AD | N/A | channel level analysis single context removal curve trending detection | Complete

## Slide 37: Reference
Team is building a common confluence page for users’ guidance, issue tracking, every meeting’ headline and all the ongoing features for AD.
More details:
  ORION AD Intro: https://confluence.micron.com/confluence/display/WWDS/ORION+AD
  Chronic OOC AD Intro: https://confluence.micron.com/confluence/display/WWDS/Chronic+AD
  Ongoing features: https://confluence.micron.com/confluence/display/WWDS/Ongoing+Features
  ORION AD Beta (RDA AD): https://tableau-apac/#/site/F10FEMFG/views/F10_QM69A_V2_RDA_OOC_SUMMARY/AD?:iid=1
  ORION AD Beta (Chronic OOC AD): https://tableau-apac/#/site/F10FEMFG/views/F10_CHRONIC_OOC_AD_SUMMARY/ChronicAD?:iid=1

## Slide 38: Acknowledgement
You may look for below teammates if you want to find more on ORION AD Beta and how they use it now.
 | F10N | F10W
RDA | Si Min | Si Min
DE | Shaun | Karin
PHOTO | Matthew Ng | Himavad
IMPLANT | Zam | Wei Jie
CVD/PVD | Ming Chuan | Yong Zheng
DF | Zheng Hoe | Lingjie
CMP | Xinqiao | Muthukumar
WP | Wei En | Yi Xuan