## Slide 1: RDA/Chronic OOC AD Introduction
F10 Data Science
Tan Peng/ Siqi/ Kaiqin

## Slide 2: Agenda
Triggering Rule
Data Source
  SPACE
  Sigma
  SWR
  QDR
  PM/CM Lead Lot
  Lot Attribute
Analysis Flow
Analysis Method
  FMEA List
  Domain knowledge
  Past Feedback
  Last OOC Check
  Time Weighted Correlation
Report
  Sections
  Report Features
Dashboard
Future Roadmap

## Slide 3: Triggering Rule
RDA OOC AD
Currently, for RDA AD, we will query past 24 hours and check whether any new OOC points.
To analyze a chart, below criteria must meet:
  chart has minimum 1 point within 24 hours
  chart has minimum 2 OOC points and 2 good points in same chart type
  chart type is mean, sigma, range and ewma-mean.

## Slide 4: Triggering Rule
Chronic OOC AD
For Chronic OOC AD triggering, we use Chronic OOC chart list from SPC team.
  for multiple chart type highlighted in the Chronic OOC chart list, the chart type with most OOC points will be analyzed by AD
To analyze a chart, below criteria must meet:
  Chart is in SPC Chronic OOC highlight list.
  Chart has minimum 2 OOC points and 2 good points in same chart type for past 30 days.
  Chart type is mean, sigma, range and ewma-mean.

## Slide 5: Data Source

## Slide 6: Data Source
SPACE Data
AD currently use Global Data Warehouse (GDW) SPACE data source from hive table.
    Databases:
      prod_mti_{region}_fab_{fab}_spc_dm
    Tables:
      prod_mti_{region}_fab_{fab}_spc_dm.T_EXT_SAMPLES_VIOL
      prod_mti_{region}_fab_{fab}_spc_dm.t_channel_def
      prod_mti_{region}_fab_{fab}_spc_dm.t_ext_samples_wafer
      prod_mti_{region}_fab_{fab}_spc_dm.t_ext_samples_lot
      prod_mti_{region}_fab_{fab}_spc_dm.t_ext_samples_calc
Query Method:
    PySpark

## Slide 7: Data Source
Sigma Data
AD currently use Global Data Warehouse (GDW) Sigma data source from HBase table.
    Databases:
      prod_mti_singapore_fab_10_sigma
    Tables:
      prod_mti_singapore_fab_10_sigma:sigma_lot_v2
      prod_mti_singapore_fab_10_sigma:sigma_wafer_v2
      prod_mti_singapore_fab_10_sigma:sigma_measurement_v2 (for future usage)
Query Method:
    HBase Thrift Server (python)

## Slide 8: Data Source
SWR Data
AD currently use Global Data Warehouse (GDW) SWR data source from Teradata table.
    Databases:
      FAB_{fab}_SWR_DM
    Tables:
      FAB_{fab}_SWR_DM.SWR_LOT
      FAB_{fab}_SWR_DM.SWR
      FAB_{fab}_SWR_DM.SPLIT_DEFINITION
      FAB_{fab}_SWR_DM.SPLIT_GROUP
      FAB_{fab}_SWR_DM.TRAV_DEF_FOR_GROUP
      FAB_{fab}_REF_DM.STEP
      FAB_{fab}_SWR_DM.WAFERS_IN_SPLIT
Query Method:
    python

## Slide 9: Data Source
QDR Data
AD currently use Global Data Warehouse (GDW) QDR data source from Teradata table.
    Databases:
      FAB_{fab}_QDR_DM
      WW_MFG_DM
    Tables:
      FAB_{fab}_QDR_DM.QDR_WAFER
      FAB_{fab}_QDR_DM.QDR_TEXT
      FAB_{fab}_QDR_DM.QDR_HEAD
      WW_MFG_DM.d_Step
Query Method:
    python

## Slide 10: Data Source
PM/CM Lead Lot Data
AD currently use Global Data Warehouse (GDW) QDR data source from Teradata table.
    Databases:
      WW_MFG_IDS_DM / WW_MFG_DM / FAB_{fab}_FT_DM
    Tables:
      Obtain pm/cm information
        WW_MFG_IDS_DM.ET_EVENT_HISTORY
        WW_MFG_IDS_DM.ET_EQUIPMENT
        WW_MFG_IDS_DM.ET_EQUIPMENT_state_for_area
        WW_MFG_IDS_DM.REF_MFG_AREA
        WW_MFG_IDS_DM.ET_EVENT_CODE_HISTORY
        WW_MFG_IDS_DM.ET_EVENT_NOTE
      Obtain lot information
        WW_MFG_DM.d_LotStepMES
        FAB_{fab}_FT_DM.FAB_LOT_HIST
        FAB_{fab}_FT_DM.FAB_LOT_EQUIP_HIST
Query Method:
    Python

## Slide 11: Data Source
Lot Attribute Data
AD currently use Global Data Warehouse (GDW) lot attribute data source from Teradata table.
    Databases:
      FAB_{fab}_FREC_DM
      FAB_{fab}_REF_DM
      WW_MFG_IDS_DM
    Tables:
      Obtain step information
        FAB_{fab}_FREC_DM.exception
        FAB_{fab}_FREC_DM.exception_member
        FAB_{fab}_FREC_DM.attr
        FAB_{fab}_FREC_DM.process_exception
        FAB_{fab}_FREC_DM.process
        FAB_{fab}_REF_DM.step
        FAB_{fab}_REF_DM.corr_item
      Obtain lot information
        WW_MFG_IDS_DM.FT_FAB_LOT_ATTR_VALUE
        WW_MFG_IDS_DM.REF_CORR_ITEM
Query Method:
    python

## Slide 12: Analysis Method

## Slide 13: Analysis Flow
Overall Design

## Slide 14: Analysis Method
FMEA List
This feature currently is only available for RDA AD.
  A list contains measurement step, process step and corresponding channel id.
  This list is prepared by RDA team so far.
  AD will check whether channel id is in the list and mark corresponding process step as FMEA step.
FMEA List Example
Measurement Step | Process Step | Channel Id
1000-82 PASS PHOTO MACRO INSP | 3010-82 PASS PHOTO | 716608
1000-82 PASS PHOTO MACRO INSP | 3010-82 PASS PHOTO | 716609
1000-82 PASS PHOTO MACRO INSP | 3010-82 PASS PHOTO | 716610
1000-82 PASS POLYIMIDE ANNEAL 2 WIS INSP | 3010-82 PASS PHOTO | 716616
1000-82 PASS POLYIMIDE ANNEAL 2 WIS INSP | 3010-82 PASS PHOTO | 716617
1000-82 PASS POLYIMIDE ANNEAL 2 WIS INSP | 3010-82 PASS PHOTO | 716618
1000-02 ALIGN MARK INSITU DRY STRIP MICRO INSP | 5200-23 PERIPH OXIDE CMP | 716622
1000-02 ALIGN MARK INSITU DRY STRIP MICRO INSP | 5200-23 PERIPH OXIDE CMP | 716623
1000-02 ALIGN MARK INSITU DRY STRIP MICRO INSP | 5200-23 PERIPH OXIDE CMP | 716624
1000-28 W0 METAL SPUTTER MICRO INSP | 3010-28 W0 PHOTO | 716628
1000-28 W0 METAL SPUTTER MICRO INSP | 3010-28 W0 PHOTO | 716631
1000-28 W0 METAL SPUTTER MICRO INSP | 3010-28 W0 PHOTO | 716632

## Slide 15: Analysis Method
Domain Knowledge
This feature currently is only available for RDA AD.
  A list contains RDA defect parameter and corresponding process step pattern.
  This list is prepared by RDA team so far.
  AD will check whether defect parameter is in the list and mark corresponding process step as Domain Knowledge step.
Domain Knowledge Example:
  “CB_32_RESIDUAL_FILM”: current loop CMP, WP or WET ETCH steps.
  “CB 19_RESIDUE”: current loop after PHOTO steps.

## Slide 16: Analysis Method
Past Feedback
This feature currently is available for both RDA AD and Chronic OOC AD.
AD will query past feedback cases for same chart and mark past feedback root cause step as feedback step

## Slide 17: Analysis Method
Last OOC Check
This feature currently is available for both RDA AD and Chronic OOC AD.
AD will focus on the latest OOC.
This method will be depreciated in near future since time weighted correlation is applied.
Only last OOC’s related information will be possible as root cause.

## Slide 18: Analysis Method
Weighted Correlation (Link)
Equal weighted
Time weighted
Time Weighted Correlation

## Slide 19: Analysis Method
This feature currently is available for both RDA AD and Chronic OOC AD.
  AD will focus on the latest OOCs.
  Toggles matches in the latest OOC time period will have much higher correlation value than early period.
  Current Rsquare value is calculated by this time weighted correlation. The higher Rsquare is, the better match between potential toggles and OOC points.
Time Weighted Correlation

## Slide 20: AD Report

## Slide 21: Report
Overview
AD report is built by HTML with JavaScript and CSS technology.
Both RDA AD and Chronic OOC AD share same report template.
It covers below sections:
  Title
  OOC Chart
  FMEA Step (RDA AD only)
  Past Feedback
  Result
  Result plots
  Feedback

## Slide 22: Report
Sections

## Slide 23: Report
Sections-OOC Chart
For header, it will display the channel, ckc and chart type.
Reference OOC lot is used in last OOC point check
This section will display below information:
  Current step: OOC step
  Process step: corresponding process step
  SPACE chart
    Red point: OOC point
    Black point: non-OOC point
    Blue dotted line: upper control limit and
            lower control limit

## Slide 24: Report
Sections-FMEA and Historical Feedback
This section will display below information:
  FMEA Table: if chart is assigned FMEA step, it will
  display corresponding process step
  Historical Feedback: if chart got feedbacked before
  the analysis, it will display latest 5 feedback.

## Slide 25: Report
Sections-Result and Plots
This section will display below information:
  Result table:
    Root cause and correlation value is shown.
  Result plot:
    Both box plot and trend plot will have same color for
    same category.
      Box plot: the first box will be colored in red and will be
      potential root cause
      Trend plot: smoothing method is used to draw the curve.
      Smoothing method is similar to Y3 kernel smoothing method.

## Slide 26: Report
Features
Download Data
  This will enable to download data which is used for AD analysis

## Slide 27: Report
Features
Open in SPACE
  This will enable user to open SPACE directly from AD report.

## Slide 28: Report
Features
Section Collapse
  This will enable user to collapse certain section.

## Slide 29: Report
Features
Click to Show Plotting Charts
  By default, the plots section only show top 3 results’ plots. Other plots user need to click on result table.
  Click one row in Result Table
  Plotting charts will be shown in Result Plots

## Slide 30: Report
Feedback
Actual Root Cause Feedback
  This will enable user to give accuracy feedback directly in report.
  4 types of feedback can be given
    Root cause found: root cause is in the result table
    Root cause not found: root cause is not in the result table
    Root cause unknow: user cannot identify root cause
    Defect misclass/ Recipe false count/ Baseline issue: chart related issue

## Slide 31: Dashboard

## Slide 32: Dashboard
SPC Chronic OOC dashboard can view AD report directly.
Both RDA AD and Chronic OOC AD has another dashboard to track AD analysis status and also view feedback status.
  AD analysis tracking by color
  AD feedback tracking
  AD accuracy tracking
Link
  RDA AD:
  Chronic OOC AD:
    F10W
    F10N

## Slide 33: Dashboard
AD analysis tracking by color
Different color shows status of Analyzed/ Not Analyzed and Feedbacked/ Not Feedbacked.
Click this will show
the AD report
Click this to refresh the dashboard
and see latest feedback status

## Slide 34: Dashboard
AD analysis tracking by color
This tab will show the past feedback by user.

## Slide 35: Dashboard
AD accuracy tracking
This tab will show the weekly and daily accuracy tracking.

## Slide 36: Future Plan
Raw chart type support
Channel level analysis for incoming toggles
DF recycle history analysis.
FD analysis
Merge all algorithm into ORION AD.